Title
MSL/RAD Critical Design Review
7b – RAD Sensor Head
Stephan Böttcher
boettcher@physik.uni-kiel.de

---
Outline
RAD Front-End-Electronics
RAD Front-End-Electronics
  - Functional Description
  - Dynamic Range Requirement
  - Photos
First Results from the Pathfinder
  - Cosmic muons

---
Overview
FEE Overview
PIN Silicon Detectors
  - 300µm
  - Anti-Refective Coating
  - Flex strips, ceramic carriers
PCB
  - 0.5mm / 1mm PI glass
  - 2 / 4 Layers
Rigid-Flex interconnect
  - PI film/PI glass
  - Bi-Lobe connectors
  - REB interface connector
Internal wireing
  - AWG32, 19-strand, PTFE
  - 0.8 mm coax, PTFE, 7-strand AWG34 core

---
Requirements
Requirements
Amplification of charge signals from Si Detectors
  - Charged particles going through Si detectors
  - Scintillation light in CsI(Tl)
  - Scintillation light in BC432m
Conditioning of the Signals for the VIRENA ASIC
  - Shaper with 2.2µs shaping time
    - Pole-zero compensation of CSA secondary time constant
    - Output signal amplitudes from 4.5mV to 3V
Dynamic Range
  - Various cases

---
CSA schematics
CSA schematics
BF862 jFET
  - very low noise
  - good match to detector capacitance
  - SOT23 plastic part
  - 3.7 mA bias current
AD8005 CFA
  - 4 mW Power
  - current feedback
  - SOT23-5 plastic part
Various gain options:
  - 1pF .. 8.2 pF
  - 100µs .. 260 µs

---
RADD board
RADD board on CsI
RADD board (low gain, 8.2pF)
Charge Sensitive Preamp on CsI
Two PEM parts: BF862, AD8005

---
FSH schematic
Shaper schematics
AD8005 CFA
2.2µs time constant
Pole-Zero compensation

---
FOV
Telescope FOV
A
Three Solid State Detectors: A, B, and C
  - Det A1: inner two hexagonal segments
  - Det A2: outer four segments
  - Det B: only innermost segment
  - Det C: two inner segments
  - AC Det C2: two segments from B, one from C
  - AC readout F1: outer segment(s) of C
B
C
D
F

---
Blockdiagram
RSH FEE Block-Diagram
17 preamps
17 shapers
3 thermistors
Power:
  - opamp power +5V, -5V
  - +5V FET bias
  - -70V Detector bias
Interface connector
  - MDM 51

---
Dynamic Telescope
Dynamic Range Telescope
From Minimally Ionizing Particles (MIPs) to Stopping Iron
  - MIP in 300µm Si (Landau distribution)
    - starting at 60 keV,
    - peak at 95 keV,
    - mean at 115 keV.
  - Stopping Iron Ion in 300µm Si:
    - 1.2 GeV
  - Dynamic Range: 20000
AD8005: 3 V output signal
Two shapers for each signal, high and low gain.
Si detector charge yield: 44mV*pF/MeV

---
Dynamic CsI
Dynamic Range CsI(Tl)
From Nuclear Gamma Lines to Stopping Iron
  - Gamma lines: A few hundred keV
  - MIPs: 25 MeV
  - Stopping Iron Ion in 3 cm CsI: 20 GeV
  - Dynamic Range: 100000
Three seperate PIN detectors reading light from CsI at different gains.
CsI(Tl) Light charge yield: 1..2 mV*pF/MeV.
Quenching factors for ions unknow, > 5.

---
Dynamic NC
Dynamic Range Neutron Channel
Neutron signals from 2 MeV to 200 MeV
Relativistic Ions
Three seperate PIN detectors reading light from BC432m Neutron Channel at different gains.
BC432m light charge yield: 0.4 mV*pF/MeV
Quenching factors for ions unknow.

---
Dynamic AC
Dynamic Range Anticoincidence
Efficient detection of MIPs in BC432m Anticoincidence
  - MIPs in 12 mm BC432m (Landau)
    - starting at 1 MeV,
    - mean at 2.4 MeV
Three seperate PIN detectors and three outer segments of C-detector reading light from CsI
Two shapers reading the sum of three CSA each.
BC432m light charge yield: 0.4 mV*pF/MeV

---
RSH Channels Summary

---
RADA board
RADA board
Top SSD readout
circuits:
  - 2 CSAs
    - A1
    - A2
  - 4 shapers
    - A1H, A1L
    - A2H, A2L
  - Thermistor
4 layers
parts on 2 sides

---
RADBC board
RADBC board
B&C SSD readout
circuits:
  - 6 CSAs
    - B, C
    - C2
    - F1a, F1b, F1c
  - 6 shapers
    - BH, BL, CH, CL
    - C2, F1
4 layers
parts on 2 sides

---
RADE board
RADE board
Neutron channel readout
circuits:
  - 3 CSAs
    - EH, EM, EL
  - 3 shapers
    - EH, EM, EL
4 layers
parts on 1 side

---
RADF board
RADF board
D shapers
F2 readout
circuits:
  - 3 CSAs
    - F2a, F2b, F2c
  - 4 shapers
    - DH, DM, DL
    - F2
RADF flight layout is in progress.
Tflex layout is in progress.

---
DIRENA test
RSH test at CAU Kiel

---
Muons Telescope
Cosmic muons in the Telescope
Selection:
  - Signal in B
  - Signal in C
  - Signal in D
Detector Area:
  - A1: 2.3 cm2
  - A2: 10 cm2

---
Muons in Scintillator
Cosmic muons in the Scintillators
Selection:
  - Signal in B
  - Signal in C
  - Signal in A1
  - no Signal in A2
for EH:
  - Signal in DH
for F2
  - Signal in EH

---
Backup
Backup Slides
Boardhouse
207Bi Spectra

---
Boardhouse
Boardhouse
The Hans Brockstedt GmbH is certificated according to DIN EN ISO 9001, MIL-PRF-55110 and MIL-P-50884 since 1992. In addition we are the first European PCB manufacturer, who is certificated acc. to the new MIL-PRF-31032/1/2/3/4 for the production line as well as for the laboratory. The first night was held by the American DESQ and the German VDE in summer 2002.
http://www.brockstedt.de

---
Bi207 e- AB
Conversion Electrons
in Detectors A and B
207Bi Source
  - e-: 480 keV, 975 keV
  - : 570 keV, 1064 keV
1 MeV e- have low probability to stop in 300µm Si, but some do.
Some e- stop in B: lines of constant sum in the scatterplot.

---
Bi207 e- ABC
Conversion Electrons
in Detectors A, B and C
Spectrum of A+B
Some e- stop in C.

---
Bi209 e- ABCD
Conversion Electrons
in Detectors A, B, C and D
Spectrum of A+B + C
The remaining e- stop in D.

---
Silicon Hit
Silicon Hit Detection
Selection:
  - DH > 15 mV
DL gain
  - 1/64 of DH gain.
CsI Light
  - DL > 1 mV

---
Gamma in CsI
207Bi gamma Spectum in CsI
Selection:
  - DH > 15 mV
  - DL > 1 mV